## Slide 1
Power Apps licence request
Preventive maintenance system · Phase 2
The PM system is live and working without it. This asks for the licence that closes the four gaps the current front end cannot, and shows what those gaps cost.
Eaton Power Quality Pvt Ltd · Pondicherry · Maintenance Engineering
Notes: Opening line: we are not asking for money to build the system. The system is built and it works. We are asking for a licence that closes four specific gaps, and here is what those gaps cost us.

## Slide 2
The system is already live
Delivered on Microsoft 365 E3. No additional licence was purchased.
14
SharePoint lists
Every PM record, indexed and versioned
9
Automated flows
Trigger, reset, escalation, digest
9
Dashboard pages
85 measures, refreshed twice daily
30
QR-tagged machines
Scan opens that machine's hub
What it does today, unattended
Adds each month's standard hours to every cell's running counter, prorated by working days when a PM reset falls mid-month
Raises a work order the morning a cell reaches 4,000 hours, or six months, whichever comes first
Resets the counter only when every machine in the cell is complete - never on a partial cell
Escalates a safety-critical finding immediately and blocks the cell from closing behind it
Figures from the system as built. Twelve months of plant data loaded and verified.
Notes: Establish credibility before asking for anything. The system works, it cost no extra licence, and it runs unattended.

## Slide 3
Four things the current front end cannot do
Microsoft Forms is a form. These are not form problems.
1
Work offline
Where the floor has no reliable signal a technician either walks to the office to submit, or writes on paper and re-keys later. Re-keyed data arrives late, and some of it never arrives at all.
2
Enforce one check at a time
Six checks on one screen can be tapped straight down the OK column. The acceptance standard - the actual limit - sits on a page the technician has to go and find.
3
Scan inside the workflow
The camera app opens a browser, which opens a form. Three context switches per machine, and any one of them can drop the pre-filled machine ID.
4
Show the technician what he needs to know
Current stock and lead time before he fits a part. Whether his machine is the last one in the cell, and the counter is about to reset. Forms shows a blank page and asks him to type.
None of these are fixed by writing a better form. They need an application.
Notes: Be specific. A vague 'better user experience' request gets declined. Four named gaps, each with a consequence.

## Slide 4
What the gap costs, measured
Twelve months of this plant's own breakdown data - not an industry benchmark.
28.1
hours of production lost
to breakdowns that happened within seven days of a completed PM on that same cell.
7 of 88 breakdowns. 9.4% of all downtime, on machines we had just maintained.
Chart: Annual production loss, 299.5 h
| Within 7 days of a PM | All other causes
Annual downtime | 28.1 | 271.4
Why this number is the right one
A breakdown days after a PM means the PM did not find what was there.
That is either a check performed too fast to see anything, or a reading nobody wrote down.
Both are execution problems at the point of capture - exactly where the four gaps are.
Compliance is 89.6% and on-time is 65.1%. Neither number would tell you any of this. A PM programme can be fully compliant and still not be working.
Source: Breakdown_Log and PM_WorkOrder, 12 months. Measure definition and verification in docs/ASSUMPTIONS.md.
Notes: This is the slide that carries the argument. 28.1 hours is measured from our own data, not estimated. If asked why it is not the 34.4 quoted earlier: a PM is now dated from its own machine scans rather than a stored column, and docs/ASSUMPTIONS.md section 9.1 shows the working.

## Slide 5
It is concentrated, not spread
Four of eight cells carry the whole of it. Those four are the pilot.
Chart: Production hours lost to post-PM breakdowns, by cell
| Curing / Autoclave | Cap Fitting | Testing & Calibration | Assembly NH | Sand Filling | Element Punching | Element Welding | Marking & Packing
Hours lost within 7 days of a PM | 10.2 | 8.4 | 4.9 | 3 | 1.6 | 0 | 0 | 0
4 cells
carry 26.5 of the 28.1 hours
15 machines
in those four cells
6 technicians
would need a licence
A pilot on those four cells tests the case before the plant commits to all eight.
Three cells lost nothing to post-PM breakdowns in twelve months. Whatever they do differently is worth copying either way.
Notes: Pre-empt 'this is a big rollout'. It is four cells and six people. It can be piloted and reversed.

## Slide 6
What changes at the machine
Same data, same lists, same flows. Only the capture changes.
Today · Microsoft Forms
Phase 2 · Canvas app
Camera app opens a browser, which opens a form
Six checks on one screen, tappable straight down the OK column
Acceptance standard on a page nobody opens
No signal means paper, then re-keying
Requests a part without seeing the stock
No idea his machine was the last in the cell
Scanner inside the app, straight to the machine
One check at a time, cannot skip an unanswered one
Acceptance standard on screen with the check
Captured offline, sent when back in range
Current stock, minimum and lead time shown first
Told when his machine closed the cell
The lists, the nine flows and the dashboard are unchanged. The app is an alternative front end over the same data - which is why Forms stays available as the fallback.
Full screen-by-screen specification already written: powerapps/CANVAS_APP_BUILD.md
Notes: The build is already specified. This is not a discovery project - the risk is low and the estimate is real.

## Slide 7
What it costs, and what it has to prevent
Two numbers the plant owns. Fill them in and the decision makes itself.
6 technicians + 2 supervisors = 8 licences
Standard connectors only - SharePoint and Office 365 Users. No Dataverse, no premium connector, no custom connector.
Licence rate | Annual, 8 users | Break-even at ₹5,000/h | Break-even at ₹10,000/h | Break-even at ₹20,000/h
₹500 / user / mo | ₹48,000 | 9.6 h (28%) | 4.8 h (14%) | 2.4 h (7%)
₹1,000 / user / mo | ₹96,000 | 19.2 h (56%) | 9.6 h (28%) | 4.8 h (14%)
₹1,500 / user / mo | ₹144,000 | 28.8 h (84%) | 14.4 h (42%) | 7.2 h (21%)
₹2,000 / user / mo | ₹192,000 | 38.4 h (112%) | 19.2 h (56%) | 9.6 h (28%)
Read a row: at ₹1,500 per user per month and ₹10,000 an hour of downtime, the licence pays for itself if it prevents 14.4 hours a year — 51% of the 28.1 hours currently lost to breakdowns that follow a PM.
Licence rates are illustrative — confirm current pricing with your Microsoft partner. Downtime cost per hour is the plant's own figure.
Notes: Do not assert a price. The grid lets them find their own row. The percentage column is the honest test: is it plausible that better capture prevents that share of post-PM breakdowns?

## Slide 8
The ask
Eight Power Apps licences, and four cells to prove it on.
1
Approve 8 licences
6 technicians, 2 supervisors. Standard connectors only.
2
Pilot on 4 cells
Curing, Cap Fitting, Testing, Assembly - the four carrying 26.5 of the 28.1 hours (94%).
3
Review after 6 months
Against post-PM breakdown hours on those four cells versus the other four.
If the answer is no, nothing breaks. The system stays live on Forms, and this stays on the shelf as a costed option with the evidence attached.
Notes: Close by removing the pressure. A request that survives a 'no' without drama is easier to say yes to. Offer the 6-month review as the reversal point.

## Slide 9
Where every number came from
So anyone can check them rather than take them on trust.
Figure | Value | Source
Annual production loss | 299.5 h | Breakdown_Log, sum of Production_Loss_Min, 12 months
Breakdowns within 7 days of a PM | 7 of 88 | Breakdown_Log paired to completed PM_WorkOrder, by cell, dated from the last machine scan
Downtime from those breakdowns | 28.1 h (9.4%) | Same 7 rows, sum of Production_Loss_Min
Concentration in four cells | 26.5 h (94%) | Curing 10.2, Cap Fitting 8.4, Testing 4.9, Assembly 3.0
PM compliance / on-time | 89.6% / 65.1% | 43 of 48 completed; 28 of 43 by the committed date
Machines in the pilot cells | 15 | Machine_Master, Active = Yes, those four cells
Technicians | 6 | Technician_Master, Active = Yes
Reproduce all of it: python tools/verify_measures.py --asof 2026-08-30
Every measure is recomputed there in plain Python, independently of the dashboard, so the two can be compared rather than one trusted. Licence rates on the previous slide are the only illustrative figures in this deck - confirm those with your Microsoft partner, and the downtime cost per hour with Finance.
Twelve months of plant data. 0 integrity errors on load; every figure re-derived from the source lists.
Notes: Offer the checkability up front. It is the difference between a number someone believes and a number someone can verify.